## Slide 1
TECHNICAL PRODUCT PORTFOLIO
Rack KVM & Remote Console Management
Detailed model selection for overseas B2B projects, system integration and procurement
TECHNICAL DATA
MODEL SELECTION
PROJECT RFQ
SP8032
SP8032
SP1708-B
SP1708-B
SP1708-C
7
catalog models
4
product families
10
application contexts
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-sp8032\sp8032-l1-r2\090_sp8032_product.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-sp8032\sp8032-l1-r2\089_sp8032_diagram.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-b\092_sp1708_b_product.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-b\091_sp1708_8port_diagram.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-c\093_sp1708_c_product.jpg

## Slide 2
RACK KVM & REMOTE CONSOLE MANAGEMENT
Application landscape
NexPro Product Intelligence · Project configurations are confirmed through RFQ
02
SP8032
SP8032
SP1708-B
Server rack management
Data center operations
Remote equipment maintenance
Local server management
Data-room racks
Maintenance consoles
Remote server access
Network equipment rooms
High-density server racks
CAT5 KVM extension
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-sp8032\sp8032-l1-r2\090_sp8032_product.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-sp8032\sp8032-l1-r2\089_sp8032_diagram.jpg
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-b\092_sp1708_b_product.jpg

## Slide 3
RACK KVM & REMOTE CONSOLE MANAGEMENT
Portfolio structure
NexPro Product Intelligence · Project configurations are confirmed through RFQ
03
SP8032 16-Port Digital KVM
1 model
SP8032
SP1708 8-Port Local VGA KVM Series
2 models
SP1708-B · SP1708-C
16-Port Remote IP KVM Series
2 models
SP5716 · SP5916
32-Port CAT5/IP KVM Series
2 models
SP8732 · SP8932
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json

## Slide 4
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP8032 · 1/1
NexPro Product Intelligence · Project configurations are confirmed through RFQ
04
SP8032
SP8032 16-Port Digital KVM
Approved parameters 1–13 of 13
PARAMETER
APPROVED SPECIFICATION
Configurations
2
Server Ports
16
Network Port
RJ45
Resolution
1920 × 1200px
Supported Systems
Windows, Linux, Mac, Sun, etc.
Power
60 W
Dimensions
400 × 440 × 44 mm
Installation
19-inch standard rack cabinet
Transmission Distance
50 m
Weight
6.6kg
User Configuration
1 local user + 2 remote users
Product series
SP8032 16-Port Digital KVM
Entity type
Product group with selectable configurations
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-sp8032\sp8032-l1-r2\090_sp8032_product.jpg

## Slide 5
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP1708-B · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
05
SP1708-B
SP1708-B 8-port local VGA KVM (1280 × 1024)
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Port Count
8
Resolution
1280 × 1024
Dimensions
485 × 570 × 44 mm
Maximum Cascade Capacity
Up to 256 devices (catalog wording: “connections 256”)
I/O Interface
PS/2 / USB dual-interface converter module
Scan Interval
1–255 seconds
System Compatibility
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Operating Temperature
0-40℃
Storage Temperature
-20-60℃
Humidity
0-80%RH, non-condensing
Warranty
3 years for main unit; 1 year for display
Product series
SP1708 8-Port Local VGA KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-b\092_sp1708_b_product.jpg

## Slide 6
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP1708-B · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
06
SP1708-B
SP1708-B 8-port local VGA KVM (1280 × 1024)
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-b\092_sp1708_b_product.jpg

## Slide 7
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP1708-C · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
07
SP1708-C
SP1708-C 8-port local VGA KVM (1920 × 1080)
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Port Count
8
Resolution
1920 × 1080
Dimensions
485 × 480 × 44 mm
Maximum Cascade Capacity
Up to 256 devices (catalog wording: “connections 256”)
I/O Interface
PS/2 / USB dual-interface converter module
Scan Interval
1–255 seconds
System Compatibility
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Operating Temperature
0-40℃
Storage Temperature
-20-60℃
Humidity
0-80%RH, non-condensing
Warranty
3 years for main unit; 1 year for display
Product series
SP1708 8-Port Local VGA KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-c\093_sp1708_c_product.jpg

## Slide 8
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP1708-C · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
08
SP1708-C
SP1708-C 8-port local VGA KVM (1920 × 1080)
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-1708\sp1708-c\093_sp1708_c_product.jpg

## Slide 9
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP5716 · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
09
SP5716
SP5716 16-port remote IP KVM
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Port Count
16
Resolution
1280 × 1024
Dimensions
485 × 570 × 44 mm
Maximum Cascade Capacity
Up to 256 devices (catalog wording: “connections 256”)
I/O Interface
PS/2 / USB dual-interface converter module
Scan Interval
1–255 seconds
System Compatibility
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Operating Temperature
0-40℃
Storage Temperature
-20-60℃
Humidity
0-80%RH, non-condensing
Warranty
3 years for main unit; 1 year for display
Product series
16-Port Remote IP KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-ip16\sp5716\095_sp5716_product.jpg

## Slide 10
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP5716 · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
10
SP5716
SP5716 16-port remote IP KVM
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-ip16\sp5716\095_sp5716_product.jpg

## Slide 11
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP5916 · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
11
SP5916
SP5916 16-Port Remote IP KVM, 600 mm Depth
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Port Count
16
Resolution
1280 × 1024
Dimensions
485 × 600 × 44 mm
Maximum Cascade Capacity
Up to 256 devices (catalog wording: “connections 256”)
I/O Interface
PS/2 / USB dual-interface converter module
Scan Interval
1–255 seconds
System Compatibility
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Operating Temperature
0-40℃
Storage Temperature
-20-60℃
Humidity
0-80%RH, non-condensing
Warranty
3 years for main unit; 1 year for display
Product series
16-Port Remote IP KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-ip16\sp5916\096_sp5916_front.jpg

## Slide 12
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP5916 · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
12
SP5916
SP5916 16-Port Remote IP KVM, 600 mm Depth
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-ip16\sp5916\096_sp5916_front.jpg

## Slide 13
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP8732 · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
13
SP8732
SP8732 32-Port CAT5 Network KVM
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Port Connection
RJ45
Port Count
32
Input / Output
PS/2 / USB dual-interface converter module
Resolution
1280 × 1024
Scan Interval
5–255 seconds
Supported Systems
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Optional Modules
CAT5 module or IP remote-access card module
Host Interface
USB / PS/2
Cascading
Supports bus and tree topologies
Dimensions
485 × 570 × 44 mm
Warranty
3 years for main unit; 1 year for display
Product series
32-Port CAT5/IP KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-cat5\sp8732\099_sp8732_product.jpg

## Slide 14
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP8732 · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
14
SP8732
SP8732 32-Port CAT5 Network KVM
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-cat5\sp8732\099_sp8732_product.jpg

## Slide 15
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP8932 · 1/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
15
SP8932
SP8932 CAT5/IP KVM (Port Description Requires Review)
Approved parameters 1–14 of 15
PARAMETER
APPROVED SPECIFICATION
Maximum Cascade Capacity
Up to 256 devices
Port Count
catalog value: 16
Input / Output
PS/2 / USB dual-interface converter module
Resolution
1280 × 1024
Scan Interval
1–255 seconds
Supported Systems
Windows, Vista, Linux, etc.
Power Input
A C100-240V, 50-60Hz, 1 A
Power Consumption
120V at 23 W; 230V at 25 W
Operating Temperature
0-40℃
Storage Temperature
-20-60℃
Humidity
0-80%RH, non-condensing
Dimensions
485 × 600 × 44 mm
Warranty
3 years for main unit; 1 year for display
Product series
32-Port CAT5/IP KVM Series
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-cat5\sp8932\100_sp8932_product.jpg

## Slide 16
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical data · SP8932 · 2/2
NexPro Product Intelligence · Project configurations are confirmed through RFQ
16
SP8932
SP8932 CAT5/IP KVM (Port Description Requires Review)
Approved parameters 15–15 of 15
PARAMETER
APPROVED SPECIFICATION
Product category
KVM
This product section contains every approved customer-facing specification field for the exact model. Missing source values are stated explicitly.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts
- D:\NexPro-Link-安放解决方案供应商网站\public\images\products\pdu-catalog\kvm-cat5\sp8932\100_sp8932_product.jpg

## Slide 17
RACK KVM & REMOTE CONSOLE MANAGEMENT
Technical selection snapshot
NexPro Product Intelligence · Project configurations are confirmed through RFQ
17
Exact model
SP8032
SP1708-C
SP5916
SP8932
Product
SP8032 16-Port Digital KVM
SP1708-C 8-port local VGA KVM (1920 × 1080)
SP5916 16-Port Remote IP KVM, 600 mm Depth
SP8932 CAT5/IP KVM (Port Description Requires Review)
Key specification 1
Configurations: 2
Port Count: 8
Port Count: 16
Maximum Cascade Capacity: Up to 256 devices
Key specification 2
Server Ports: 16
Resolution: 1920 × 1080
Resolution: 1280 × 1024
Port Count: catalog value: 16
Application fit
Server rack management · Data center operations · Rem…
Local server management · Data-room racks · Maintenan…
Remote server access · Data center operations · Netwo…
High-density server racks · CAT5 KVM extension · Data…
Use the detailed Word specification documents for complete approved attributes and family variant tables.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json

## Slide 18
RACK KVM & REMOTE CONSOLE MANAGEMENT
Approved model register
NexPro Product Intelligence · Project configurations are confirmed through RFQ
18
SP8032
SP1708-B
SP1708-C
SP5716
SP5916
SP8732
SP8932
7 exact website model records shown on this page · 7 total for this product line
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\NexPro-Link-安放解决方案供应商网站\src\data\products.ts

## Slide 19
RACK KVM & REMOTE CONSOLE MANAGEMENT
Procurement and RFQ checklist
NexPro Product Intelligence · Project configurations are confirmed through RFQ
19
01
Quantity & mix
Confirm by model and project quantity
02
Lead time
Confirm after configuration review
03
Shipping basis
Confirm in project quotation
04
OEM / ODM
To be confirmed
Include in your inquiry
Exact model or required function
Estimated quantity
Destination country or port
Required interfaces / accessories
Documentation and OEM/ODM needs
Final configuration, availability and commercial terms are confirmed in the project quotation.
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json

## Slide 20
READY FOR THE PROJECT LIST
Share your requirements.
We will shortlist the right models.
Rack KVM & Remote Console Management
REQUEST A PROJECT QUOTATION
NexPro · 20
Notes: [Sources]
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0203\product-artifact-manifest.json
- D:\Nexpro-link 产品数据库\artifacts\NPL-DB-0304\assets\nexpro-technical-background-v1.png